## Slide 1: AI-Based Electrical Insulation Degradation Classification
Using Leakage Current Patterns
Internship Capstone Project

## Slide 2: Problem Statement
Insulation condition may influence leakage-current waveform patterns.
Goal: classify signals as Healthy, Moderately Degraded, or Severely Degraded.
Deliver an explainable workflow with model evaluation and a dashboard.

## Slide 3: Objectives
Create labelled signal windows and validate input quality.
Extract time-domain and frequency-domain features.
Train and compare two machine-learning models.
Evaluate on held-out test data and visualize results.

## Slide 4: Dataset and Assumptions
540 simulated windows; 1000 samples per window; 1000 Hz sampling.
Three balanced classes with controlled amplitude, noise, harmonics and transient pulses.
Important: data are simulated, not measured experimental leakage current.
Scores demonstrate software behavior, not real-world diagnostic capability.

## Slide 5: System Architecture
Signal windows → preprocessing → feature extraction
Stratified train/test split (75% / 25%)
Random Forest + Histogram Gradient Boosting
Metrics and confusion matrices → Streamlit dashboard

## Slide 6: Signal Features
RMS, peak absolute current, standard deviation, mean absolute current
Crest factor, skewness, kurtosis, zero-crossing rate
Welch PSD: dominant frequency, spectral centroid, high-frequency power ratio
Dashboard also plots the waveform and FFT magnitude spectrum.

## Slide 7: Models
Random Forest: ensemble of decision trees; balanced class weights.
Histogram-based Gradient Boosting: sequential tree-based learner.
Both models use the same feature table and fixed random seed.
Held-out test data are not used during fitting.

## Slide 8: Evaluation
Accuracy, class-wise precision, recall and F1-score
Confusion matrix to inspect class-specific errors
Metrics are saved to reports/evaluation_metrics.json.
Synthetic test performance must not be presented as field accuracy.

## Slide 9: Dashboard
Dataset class counts and record selector
Leakage-current waveform and FFT spectrum
Predicted class and class probabilities where available
Extracted feature table for interpretation

## Slide 10: How to Run
pip install -r requirements.txt
python src/train_model.py
streamlit run src/dashboard.py
Use Python 3.10+; local browser opens the dashboard.

## Slide 11: Limitations and Future Work
Synthetic patterns simplify real electrical behavior.
Obtain expert-labelled measured data for credible validation.
Test across independent devices/specimens and operating conditions.
Add uncertainty handling, signal-quality checks and model calibration.

## Slide 12: Conclusion
End-to-end prototype covers signal processing, ML, evaluation and visualization.
Modular source code and dataset are included.
Real-world use requires measured data and qualified electrical safety review.